## Slide 1
Sam Burden
Assistant Professor
Electrical Engineering
University of Washington
Seattle, WA USA
http://faculty.uw.edu/sburden
Predictive dynamical models for sensorimotor control

## Slide 2
sensorimotor integration is hard!

## Slide 3
sensorimotor control system:
robotic teleoperation
sensory feedback
motor control inputs
sensory feedback
Chiawakum Creek Fire near Lake Wenatchee, WA © Michael Stanford 2015 http://yourshot.nationalgeographic.com/photos/4181903/
two decision-making agents in a dynamic world

## Slide 5
  overreliance on enhanced safety features in cars
    Rudin-Brown, Parker Traffic Psych. Behav. 2004;
    Moore, Zuby Proc. Enhanced Safety Vehicles 2013
embedding humans amid automation
  pilot-induced oscillations in rotory & fixed-wing aircraft
    McRuer, Krendal 1974; Hess J. Guid. Cont. Dyn. 1997
    Pavel et al. Prog. Aero. Sci. 2013
naïve coupling can lead to performance loss
ranging from mild to catastrophic

## Slide 6
intervening in a sensorimotor control system
sensory feedback
motor control inputs
sensory feedback
any intervention alters the sensorimotor loop
provably-safe interventions will require predictive models for sensorimotor loops

## Slide 7
today’s talk:
predictive dynamical models
for sensorimotor control
internal models
terra-dynamics
M, M-1

## Slide 8
today’s talk:
predictive dynamical models
for sensorimotor control
internal models
terra-dynamics
M, M-1

## Slide 9
predictable behavior from internal models
forward model
inverse model
  predicts sensory effects of motor actions
    Sutton, Barto Psych. Rev. 1981
    Jordan, Rumelhart Cog. Sci. 1992
    Wolpert, Ghahramani, Jordan Science 1995
  computes action expected to yield desired behavior
    Kawato Curr. Opin. Neurobio. 1999
    Thoroughman, Shadmehr Nature 2000
    Conditt, Mussa-Ivaldi PNAS 1999
Notes: replace text with cartoon

## Slide 10
predictable behavior from internal models
forward model
inverse model
  theoretical and empirical evidence for pairing of forward + inverse models
    Bhushan, Shadmehr Bio. Cybern. 1999; Sanner, Kosha Bio. Cybern. 1999
+
  parallels in control theory, robotics, artificial intelligence: adaptive control, internal model principle, learning
    Francis, Wonham Automatica 1976; Sastry, Bodson Prentice Hall 1989
    Sutton, Barto, Williams IEEE CSM 1992; Atkeson, Schaal ICML 1997
    Papavassiliou, Russell IJCAI 1999
Notes: replace text with cartoon

## Slide 11
Forward model ( M : U  Y ): static vs. dynamic
  static map (linear or nonlinear)
    Hanuschkin, Ganguli, Hahnloser Front. Neural Circ. 2013
    Giret, Kornfeld, Ganguli, Hahnloser PNAS 2014
  dynamic map depends on
  intermediate state
    Thoroughman, Shadmehr Science 2000
    Wolpert, Diedrichsen, Flanagan Nature Neurosci. 2011
Inverse model ( M-1 : Y  U ): hard to define
  static map may fail to be one-to-one or onto
  dynamic map may be acausal or need state estimate
instantiating internal models

## Slide 12
dynamic forward model
  forward model is simpler in (x,z) coordinates
*strict relative degree – easily satisfied for mechanical systems
  under a technical condition* we change coordinates to
  start with forward model in control-affine form

## Slide 13
dynamic inverse model
  start with simplified forward model
*augment with feedback to correct for initial condition error
  to obtain inverse model, apply input ud that matches* g—th derivative of desired output yd :

## Slide 14
pairing forward + inverse models
  closed-loop dynamics have undesirable property:
  states in z are unobservable
  generally impossible to compute inverting input ud using sensor data
  by restricting system dynamics, can bypass this issue:
Robinson, Scobee, Burden, Sastry Proc. SPIE-DSS (to appear, 2016)
Dynamic inverse models in human-cyber-physical systems
Theorem (Robinson, Scobee, Burden, Sastry):
If forward M and inverse M-1 are stable models,
then feedforward input from internal model
asymptotically inverts system’s dynamics.

## Slide 15
Theorem implies:
  for stable model pair, trajectories x1 and x2 converge to
  feedforward input “asymptotically inverts” dynamics
inversion with stable model pair (M, M-1)
M, M-1
input ud
output y
Robinson, Scobee, Burden, Sastry Proc. SPIE-DSS (to appear, 2016)
Dynamic inverse models in human-cyber-physical systems

## Slide 16
if inverse model predicts human’s behavior
  task hH is an input to the unobservable dynamics z
  by measuring human’s input uH, can infer task hH
  automation can solve optimal control problem to improve performance as measured by

## Slide 17
application: provably-safe interventions
sensory feedback
motor control inputs
sensory feedback
any intervention alters the sensorimotor loop
if inverse model predicts human’s behavior,
the above intervention is provably-safe

## Slide 18
today’s talk:
predictive dynamical models
for sensorimotor control
internal models
terra-dynamics
M, M-1

## Slide 19
today’s talk:
predictive dynamical models
for sensorimotor control
internal models
terra-dynamics
M, M-1

## Slide 20
  locomotion through fluid governed by continuous hydro- and aero-dynamics
  locomotion on land governed by intermittent terra-dynamics
Tytell, Standen, Lauder JEB 2008
Cory, Moore, Tedrake B&B 2014
Libby, Moore, Chang-Siu, Cohen, Jusufi, Full Nature 2012
Johnson, Koditschek ICRA 2013
Vogel Life in moving fluids 1996
Li, Zhang, Goldman Science 2015
legged locomotion involves intermittent interaction

## Slide 21
Muybridge 1887 (reprinted by Dover in 1957)
Johnson, Burden, Koditschek IJRR (in review, 2016)
A hybrid systems model for simple manipulation and self-manipulation systems
parsimonious models are piecewise-defined

## Slide 22
near-simultaneous footfalls are ubiquitous

## Slide 23
near-simultaneous footfalls are ubiquitous

## Slide 24
Hyun, Seok, Lee, Kim IJRR 2014
Galloway, Haynes, Ilhan, Johnson, Knopf, Lynch, Plotnick, White, Koditschek UPenn 2010
near-simultaneous footfalls are ubiquitous

## Slide 25
inconsistencies arise when limbs are rigid
  hand with rigid fingers exhibits 5 different post-grasp outcomes
  quadruped with rigid legs exhibits 3 distinct trot gaits
Remy, Buffington, Siegwart IJRR 2010
Hürmüzlü and Marghitu IJRR 1994, JAM 1995
rigid limbs yield inconsistent terra-dynamics

## Slide 26
rigid vs elastic limbs
rigid limbs
elastic limbs
elastic limbs yield consistent terra-dynamics

## Slide 27
Burden, Revzen, Sastry IEEE TAC 2015 (arXiv:1308.4158)
Model reduction near periodic orbits of hybrid dynamical systems
reduction
Theorem: n-leg polyped reduces to lateral leg-spring (LLS) after 1 stride

## Slide 28
stabilization
Burden, Sastry, Koditschek, Revzen SIADS (in review, 2016; arXiv:1407.1775)
Event-Selected Vector Field Discontinuities Yield Piecewise-Differentiable Flows
Theorem: near-simultaneous footfalls passively stabilize rotations (e.g. pitch)

## Slide 29
today’s talk:
predictive dynamical models
for sensorimotor control
internal models
terra-dynamics
M, M-1

## Slide 30
Jindrich, Full Journal of Experimental Biology 205(18):2803-2823 2002
Carrier, Walter, Lee Journal of Experimental Biology 204(22):3917-3926 2001
(how) can we predict experimental outcomes?
Notes: As a dynamicist and control theorist, I find the kinds of perturbations and treatments employed by experimentalists fascinating.
I’ve spent my career modeling and controlling systems whose dynamics are poorly-understood; neuromechanics is a rich frontier for unmodeled dynamics.

## Slide 31
real-time

## Slide 32: lateral perturbation experimental setup
platform accelerates laterally at 0.6 ± 0.1 g in a 0.1 sec interval providing a 50 ± 3 cm/sec specific impulse, then maintains velocity.
cockroach running speed:
36 ± 8 cm/sec
stride frequency:
12.6 ± 2.9 Hz
(~80ms per stride)
trackway
camera
diffuser
mirror
magnetic lock
animal motion
cart
cart motion
rail
pulley
mass
cable
elastic
ground
Revzen, Burden, Moore, Mongeau, Full Biological Cybernetics 107(2):179-200 2013

## Slide 33
20x

## Slide 34
real-time
constant frequency
frequency change
neural feedback occurs at a delay;
how does feedback alter recovery?
Revzen, Burden, Moore, Mongeau, Full Bio. Cyber. 2013
Instantaneous kinematic phase reflects neuromechanical response to lateral perturbations of running cockroaches

## Slide 35
cart acceleration induces equal & opposite animal acceleration
perturbations
treatments
(how) can we predict experimental outcomes?

## Slide 36
Revzen & Guckenheimer
J. Royal Society Interface 9(70) 2012
Full, Kubow, Schmitt, Holmes, Koditschek Integ and Comp Bio 42(1) 2002
Perturbation remaining per stride
0
0.5
1.5
1
2
Nondimensional Moment of Inertia
Animal
More Stable
Less Stable
0.2
0.4
0.6
0.8
1.0
data-driven
models of dynamic legged locomotion
analytical

## Slide 37
perturbing data-driven model
Revzen, Guckenheimer J. Roy. Soc. Int. 2012
Revzen, Guckenheimer Phys. Rev. E 2008
perturbations
treatments
?
Notes: For example the previous empirical results are a simple data-driven model. In that model we estimate a phase statistic so that phase then becomes your predictor. So in this picture at any point along the periodic behavior we get a distribution of animal state.

## Slide 38
perturbing analytical model
overwhelming experimental perturbation
Notes: Limitation of simple analytical models: predictions become invalid away from steady-state behavior
LLS made to steady-state periodic locomotion. The perturbation takes the model into a regime where we cant even keep simulating.
We tried to make this model work with minor alterations, but with no success the experimental perturbation overwhelms the model.

## Slide 39
lateral acceleration

## Slide 40
lateral acceleration
non-zero acceleration at step transition

## Slide 41
Hypothesis: body acceleration determined
by pose relative to stance tripod

## Slide 42
proposed model structure
body state comprised of:
  forward position
  lateral position
  body orientation
body acceleration arises from spring-like potential

## Slide 43
introducing perturbations and treatments
  forward position
  lateral position
  body orientation
body acceleration influenced by
  perturbation (e.g. lateral acceleration a(t) )
  treatment (e.g. inertia distribution M )

## Slide 44
lateral acceleration
non-zero acceleration at step transition

## Slide 45
Today’s talk:
predictive dynamical models
for sensorimotor control
internal models
terra-dynamics
M, M-1

## Slide 46
robotic teleoperation

## Slide 48
robotic teleoperation
future work:
dynamic tele-manipulation & tele-locomotion

## Slide 49
human interaction with the physical world
is increasingly mediated by automation
humans are the enabling technology

## Slide 50
Aaron Johnson
Dan Koditschek
Shankar Sastry
Shai Revzen
J-M Mongeau
Bob Full
Talia Moore
Bora Banjanin
sburden@uw.edu
http://faculty.uw.edu/sburden
thank you!
Dexter Scobee
Ryan Robinson
support