## Slide 1
Predictive dynamical models for intermittent contact
BioRobotics Lab
http://brl.ee.washington.edu
Sam Burden
Assistant Professor
Electrical Engineering
University of Washington
Seattle, WA USA
http://faculty.uw.edu/sburden
AMP Lab
http://depts.washington.edu/amplify

## Slide 2
Johnson, Burden, Koditschek IJRR 2016
A hybrid systems model for simple
manipulation and self-manipulation systems
Muybridge 1887 (reprinted by Dover in 1957)
simple models for locomotion and
manipulation are piecewise-defined
Theorem (Ballard):
trajectories exist uniquely for all forward time
Ballard Archive Rat. Mech. Anal. 2000
Dynamics of Discrete Mechanical Systems with Perfect Unilateral Constraints
  limbs in contact with ground
  ground penetration constraints
  continuous dynamics
  impact dynamics

## Slide 4
Theorem (Aizerman & Gantmacher et al):
when contact mode sequence is given,
final state varies differentiably w.r.t. initial state
Aizerman & Gantmacher 1958
Quarterly Journal of Mechanics and Applied Mathematics
Determination of Stability by Linear Approximation of a Periodic Solution of a System of Differential Equations with Discontinuous Right-Hand Sides
Grizzle, Abba, Plestan IEEE TAC 2002
Di Bernardo, Budd, Kowalczyk, Champneys Springer 2008
Burden, Revzen, Sastry IEEE TAC 2015

## Slide 5
Theorem (Remy et al):
for simultaneous impacts, final state generally
varies discontinuously w.r.t. initial state
Remy, Buffington, Siegwart
International Journal of Robotics Research 2010
Stability Analysis of Passive Dynamic Walking of Quadrupeds
Hürmüzlü and Marghitu
International Journal of Robotics Research 1994
Rigid Body Collisions of Planar Kinematic Chains With Multiple Contact Points

## Slide 6
Theorem (Pace, Burden):
if constraints are orthogonal (in body frame),
final state varies differentiably* w.r.t. initial state
  * technically piecewise-differentiably; for details, read:
Burden, Sastry, Koditschek, Revzen SIADS 2016 (arXiv:1407.1775)
Event-Selected Vector Field Discontinuities Yield Piecewise-Differentiable Flows
Pace, Burden (arXiv:1610.05645)
Piecewise-differentiable trajectory outcomes in mechanical systems subject to unilateral constraints

## Slide 7
1. pathologies in simple predictive models
— should we change our models or our robots?
challenges for predictive dynamical modeling of intermittent contact
2. data-driven predictive models
— (how) should we derive models directly from data?

## Slide 8
when limbs are rigid, final state generally
varies discontinuously with respect to initial conditions when contact mode sequence varies
  — scalable (gradient-based) algorithms for learning or control cannot change contact mode sequence

## Slide 9
Hyun, Seok, Lee, Kim IJRR 2014
Galloway, Haynes, Ilhan, Johnson, Knopf, Lynch, Plotnick, White, Koditschek UPenn 2010
do we observe discontinuous outcomes?

## Slide 10
when limbs are compliant, final state varies differentiably with respect to initial conditions
when contact mode sequence varies
  — scalable (gradient-based) algorithms for learning or control can change contact mode sequence

## Slide 12
Aaron Johnson
Dan Koditschek
Shankar Sastry
Shai Revzen
sburden@uw.edu
http://faculty.uw.edu/sburden
thank you!
ARO YIP #W911NF-16-1-0158: Predictive models for sensorimotor control of legged locomotion
collaborators
Andrew Pace