## Slide 1
Predictive dynamical models
for human sensorimotor control
of teleoperated robots
BioRobotics Lab
http://brl.ee.washington.edu
Sam Burden
Assistant Professor
Electrical Engineering
University of Washington
Seattle, WA USA
http://faculty.uw.edu/sburden
AMP Lab
http://depts.washington.edu/amplify

## Slide 2
human interaction with the physical world
is increasingly mediated by automation
Human-Cyber-Physical Systems (HCPS)

## Slide 3
Human-Cyber-Physical System:
robotic teleoperation
sensory feedback
motor control inputs
sensory feedback
Chiawakum Creek Fire near Lake Wenatchee, WA © Michael Stanford 2015 http://yourshot.nationalgeographic.com/photos/4181903/

## Slide 4
roles for humans and automation
legal, ethical, and political concerns
ensure humans will remain in-the-loop
Nothwang, Robinson, Burden, McCourt, Curtis IEEE Resilience Week 2016
The Human Should be Part of the Control Loop?

## Slide 5
  overreliance on enhanced safety features in cars
    Rudin-Brown, Parker Traffic Psych. Behav. 2004;
    Moore, Zuby Proc. Enhanced Safety Vehicles 2013
embedding humans amid automation
  pilot-induced oscillations in rotory & fixed-wing aircraft
    McRuer, Krendal 1974; Hess J. Guid. Cont. Dyn. 1997
    Pavel et al. Prog. Aero. Sci. 2013
naïve coupling can lead to performance loss
ranging from mild to catastrophic

## Slide 6
intervening in Human-Cyber-Physical Systems
sensory feedback
motor control inputs
sensory feedback
any intervention alters the sensorimotor loop
safe intervention requires validated
predictive models for sensorimotor loops

## Slide 7
predictable behavior from internal models
forward model
inverse model
  predicts sensory effects of motor actions
    Sutton, Barto Psych. Rev. 1981
    Jordan, Rumelhart Cog. Sci. 1992
    Wolpert, Ghahramani, Jordan Science 1995
  computes action expected to yield desired behavior
    Kawato Curr. Opin. Neurobio. 1999
    Thoroughman, Shadmehr Nature 2000
    Conditt, Mussa-Ivaldi PNAS 1999
Notes: replace text with cartoon

## Slide 8
predictable behavior from internal models
forward model
inverse model
  theoretical and empirical evidence for pairing of forward + inverse models
    Bhushan, Shadmehr Bio. Cybern. 1999; Sanner, Kosha Bio. Cybern. 1999
+
  parallels in control theory, robotics, artificial intelligence: adaptive control, internal model principle, learning
    Francis, Wonham Automatica 1976; Sastry, Bodson Prentice Hall 1989
    Sutton, Barto, Williams IEEE CSM 1992; Atkeson, Schaal ICML 1997
    Papavassiliou, Russell IJCAI 1999
Notes: replace text with cartoon

## Slide 9
Forward model ( M : U  Y ): static vs. dynamic
  static map (linear or nonlinear)
    Hanuschkin, Ganguli, Hahnloser Front. Neural Circ. 2013
    Giret, Kornfeld, Ganguli, Hahnloser PNAS 2014
  dynamic map depends on
  intermediate state
    Thoroughman, Shadmehr Science 2000
    Wolpert, Diedrichsen, Flanagan Nature Neurosci. 2011
Inverse model ( M-1 : Y  U ): hard to define
  static map may fail to be one-to-one or onto
  dynamic map may be acausal or need state estimate
instantiating internal models

## Slide 10
dynamic forward model
  forward model is simpler in (x,z) coordinates
*strict relative degree – easily satisfied for mechanical systems
  under a technical condition* we change coordinates to
  start with forward model in control-affine form

## Slide 11
dynamic inverse model
  start with simplified forward model
*augment with feedback to correct for initial condition error
  to obtain inverse model, apply input ud that matches* g—th derivative of desired output yd :

## Slide 12
pairing forward + inverse models
  closed-loop dynamics have undesirable property:
  states in z are unobservable
  generally impossible to compute inverting input ud using sensor data
  by restricting system dynamics, can bypass this issue:
Robinson, Scobee, Burden, Sastry SPIE-DSS 2016
Dynamic inverse models in human-cyber-physical systems
Theorem (Robinson, Scobee, Burden, Sastry):
If forward M and inverse M-1 are stable models,
then feedforward input from internal model
asymptotically inverts system’s dynamics.

## Slide 13
Theorem implies:
  for stable model pair, trajectories x1 and x2 converge to
  feedforward input “asymptotically inverts” dynamics
inversion with stable model pair (M, M-1)
M, M-1
input ud
output y
Robinson, Scobee, Burden, Sastry SPIE-DSS 2016
Dynamic inverse models in human-cyber-physical systems

## Slide 14
testing forward + inverse models
  subjects use 1-dimensional input device to control vertical cursor position to track specified reference

## Slide 15
do humans use inverse models?

## Slide 16
do humans use PD control?

## Slide 17
do humans use PD control?
  output nonlinearity changes learned model, leaves predicted input unaffected

## Slide 18
data analysis and visualization
  each assay consists of 10 up and down references with each of 2 magnitudes (10%, 20% display height)

## Slide 19
data analysis and visualization
  each assay consists of 10 up and down references with each of 2 magnitudes (10%, 20% display height)

## Slide 20
data analysis and visualization
  to visualize the data, we flip down trials and shift the baseline to coincide for all trials

## Slide 21
data analysis and visualization
  to visualize the data, we flip down trials and shift the baseline to coincide for all trials

## Slide 22
data analysis and visualization
  to assess subject performance, we visualize the interquartile range (i.e. 25th—75th percentiles)

## Slide 23
results: first-order model
operator outputs enclose reference,
but operator inputs do not

## Slide 24
results: zero dynamics, nonlinearities
zero dynamics increase input error;
nonlinearities decrease input error (?)

## Slide 25
Human-Cyber-Physical System:
robotic teleoperation

## Slide 27
future:
dynamic tele-manipulation & tele-locomotion
Human-Cyber-Physical System:
robotic teleoperation

## Slide 28
Darrin Howell
Cydney Beckwith
Shankar Sastry
Eatai Roth
sburden@uw.edu
http://faculty.uw.edu/sburden
thank you!
Dexter Scobee
Ryan Robinson
Mike McCourt
Will Nothwang
CPS #1565529: Provably-safe interventions for Human-Cyber-Physical Systems
ONR #N00014-13-1-0341:
Embedded Humans MURI