## Slide 1
Toward telelocomotion:
human sensorimotor control
of contact-rich robot dynamics
BioRobotics Lab
http://brl.ee.washington.edu
Sam Burden
Assistant Professor
Electrical & Computer Engineering
University of Washington
Seattle, WA USA
http://faculty.uw.edu/sburden
AMP Lab
http://depts.washington.edu/amplify

## Slide 2
Hannaford, Rosen, Friedman, King, Roan, Cheng, Glozman, Ma, Kosari, White IEEE Tran Biomed Eng 2013 Raven-II: An Open Platform for Surgical Robotics Research
Wodlinger, Downey, Tyler-Kabara, Schwartz, Boninger, Collinger J Neural Eng 2015
Ten-Dimensional Anthropomorphic Arm Control in a Human Brain-Machine Interface
Collins, Wiggin, Sawicki Nature 2015
Reducing the Energy Cost of Human Walking Using an Unpowered Exoskeleton
human interaction with the physical world
is increasingly mediated by machines
legal, ethical, and political concerns
ensure humans will remain in-the-loop
Nothwang, Robinson, Burden, McCourt, Curtis IEEE Resilience Week 2016
The Human Should be Part of the Control Loop?

## Slide 3
human/machine system:
robot teleoperation
Chiawakum Creek Fire near Lake Wenatchee, WA © Michael Stanford 2015 http://yourshot.nationalgeographic.com/photos/4181903/
human motor outputs
human sensory inputs

## Slide 4
robots struggle with contact-rich dynamics

## Slide 5
  overreliance on enhanced safety features in cars
    Rudin-Brown, Parker Traffic Psych. Behav. 2004;
    Moore, Zuby Proc. Enhanced Safety Vehicles 2013
coupling humans and machines
  pilot-induced oscillations in rotory & fixed-wing aircraft
    McRuer, Krendal 1974; Hess J. Guid. Cont. Dyn. 1997
    Pavel et al. Prog. Aero. Sci. 2013
naïve coupling can lead to performance loss
ranging from mild to catastrophic

## Slide 6
human/machine system:
robot teleoperation
Chiawakum Creek Fire near Lake Wenatchee, WA © Michael Stanford 2015 http://yourshot.nationalgeographic.com/photos/4181903/
human motor outputs
human sensory inputs
how do we enable humans to learn and control
contact-rich robot dynamics?

## Slide 7
how do we enable humans to learn and control
contact-rich robot dynamics?
today’s talk:
contact-rich robot
terradynamics
human sensorimotor
learning and control

## Slide 8
how do we enable humans to learn and control
contact-rich robot dynamics?
today’s talk:
human sensorimotor
learning and control
contact-rich robot
terradynamics

## Slide 9
  locomotion through fluid governed by continuous hydro- and aero-dynamics
  locomotion on land governed by intermittent terra-dynamics
Tytell, Standen, Lauder JEB 2008
Cory, Moore, Tedrake B&B 2014
Libby, Moore, Chang-Siu, Cohen, Jusufi, Full Nature 2012
Johnson, Koditschek ICRA 2013
Vogel Life in moving fluids 1996
Li, Zhang, Goldman Science 2015
legged locomotion involves contact-rich dynamics

## Slide 10
Johnson, Burden, Koditschek IJRR 2016 (arXiv:1502.01538)
A hybrid systems model for simple manipulation and self-manipulation systems
  limbs in contact with ground
  ground penetration constraints
  continuous dynamics
  impact dynamics
Muybridge 1887 (reprinted by Dover in 1957)
simple models are piecewise-defined (hybrid)

## Slide 13
Theorem (Aizerman & Gantmacher et al):
if contact sequence doesn’t change,
final state varies differentiably w.r.t. initial state
Aizerman & Gantmacher 1958
Quarterly Journal of Mechanics and Applied Mathematics
Determination of Stability by Linear Approximation of a Periodic Solution of a System of Differential Equations with Discontinuous Right-Hand Sides
Grizzle, Abba, Plestan IEEE TAC 2002
Di Bernardo, Budd, Kowalczyk, Champneys Springer 2008
Burden, Revzen, Sastry IEEE TAC 2015

## Slide 14
Hyun, Seok, Lee, Kim IJRR 2014
Galloway, Haynes, Ilhan, Johnson, Knopf, Lynch, Plotnick, White, Koditschek UPenn 2010
what if contact sequence can vary?

## Slide 16
Theorem (Remy et al):
near simultaneous impacts, final state generally
varies discontinuously w.r.t. initial state
Remy, Buffington, Siegwart
International Journal of Robotics Research 2010
Stability Analysis of Passive Dynamic Walking of Quadrupeds
Hürmüzlü and Marghitu
International Journal of Robotics Research 1994
Rigid Body Collisions of Planar Kinematic Chains With Multiple Contact Points

## Slide 17
inconsistencies arise when limbs are coupled
  hand with rigid fingers exhibits 5 different post-grasp outcomes
  quadruped with rigid legs exhibits 3 distinct (near-)trot gaits
Remy, Buffington, Siegwart IJRR 2010
Hürmüzlü and Marghitu IJRR 1994, JAM 1995
rigidly coupled limbs
 post-impact inconsistencies

## Slide 18
coupled vs decoupled limbs
coupled limbs
decoupled limbs
inertially decoupled limbs
 post-impact consistency

## Slide 19
coupled
limbs

## Slide 20
decoupled
limbs

## Slide 21
Theorem (Pace & Burden):
if limbs are inertially decoupled, final state varies
piecewise-differentiably w.r.t. initial state
Burden, Sastry, Koditschek, Revzen SIADS 2016 (arXiv:1407.1775)
Event-Selected Vector Field Discontinuities Yield Piecewise-Differentiable Flows
Pace & Burden HSCC 2017 (arXiv:1610.05645)
Piecewise-differentiable trajectory outcomes in mechanical systems subject to unilateral constraints
Pace & Burden ICRA 2017 (arXiv:1609.04056)
Decoupled limbs yield differentiable trajectory outcomes through intermittent contact

## Slide 22
trajectories vary continuously ….

## Slide 23
trajectories vary continuously ….
… do they
expand
or
contract?

## Slide 24
trajectories vary continuously ….
… do they
expand
or
contract?

## Slide 25
d(
,
)=0
Burden, Gonzalez, Vasudevan, Bajcsy, Sastry IEEE TAC 2015
Metrization and simulation of controlled hybrid systems
aside: how to measure distance?
Theorem (Burden, Gonzalez, Vasudevan, et al):
d(x -, x +) = 0 determines a distance metric
compatible with topological quotient x - ~ x +

## Slide 26
Theorem (Lohmiller & Slotine): if the
or
dynamics are infinitesimally contractive,
or
then the dynamics are globally contractive,
i.e. distances decrease at an exponential rate
contraction in classical dynamics
Lohmiller, Slotine Automatica 1998
On contraction analysis for nonlinear systems
continuous-time
discrete-time

## Slide 27
Johnson, Burden, Koditschek IJRR 2016 (arXiv:1502.01538)
A hybrid systems model for simple manipulation and self-manipulation systems
  continuous-time
  discrete-time (impact)
continuous-time and discrete-time interact in contact-rich dynamics
contact-rich dynamics
  limbs in contact with ground
  ground penetration constraints

## Slide 29
can’t look at discrete-time alone …

## Slide 30
Aizerman & Gantmacher Quarterly Journal of Mechanics and Applied Mathematics 1958
Determination of Stability by Linear Approximation of a Periodic Solution of a System of Differential Equations with Discontinuous Right-Hand Sides
can’t look at discrete-time alone …
need interaction w/ continuous-time:

## Slide 31
Theorem (Burden, Libby, Coogan): if the
and
dynamics are infinitesimally contractive,
and
then combined dynamics globally contractive,
i.e. distances decrease at an exponential rate
contraction in contact-rich dynamics
continuous-time
discrete-time
Burden, Libby, Coogan (arXiv: 1804.04122v2)
On infinitesimal contraction analysis for hybrid systems

## Slide 32
Burden, Libby, Coogan (arXiv: 1804.04122v2)
On infinitesimal contraction analysis for hybrid systems
decoupled
limbs
decoupled how?
body
foot
elastic: expansive
body
foot
viscoelastic: contractive
body
foot
rigid: discontinuous

## Slide 33
how do we enable humans to learn and control
contact-rich robot dynamics?
today’s talk:
human sensorimotor
learning and control
takeaway:
contractive contact-rich robot dynamics

## Slide 34
how do we enable humans to learn and control
contact-rich robot dynamics?
today’s talk:
human sensorimotor
learning and control
takeaway:
contractive contact-rich robot dynamics

## Slide 35
y
output
u
input
reference
r
d
disturbance
McRuer, Krendel J Franklin Institute 1959
The Human Operator as a Servo System Element
McRuer Automatica 1980
Human Dynamics in Man-Machine Systems
y
u
r
d

## Slide 36
McRuer, Krendel J Franklin Institute 1959
The Human Operator as a Servo System Element
McRuer Automatica 1980
Human Dynamics in Man-Machine Systems
F
B
+
+
M
r
f
d
b
+
-
e
y
human/machine system
H
u
predicting behavior: what’s in ?
H

## Slide 37
  theoretical and empirical evidence for pairing of system + inverse models
    Bhushan, Shadmehr Bio Cybern 1999;
    Sanner, Kosha Bio Cybern 1999
predicting behavior: what’s in ?
system model
inverse model
+
  parallels in control theory, artificial intelligence: adaptive control, internal model principle, reinforcement learning
    Francis, Wonham Automatica 1976; Sastry, Bodson Prentice Hall 1989
    Sutton, Barto, Williams IEEE CSM 1992; Atkeson, Schaal ICML 1997
    Papavassiliou, Russell IJCAI 1999
feedforward
H
Notes: replace text with cartoon

## Slide 38
F
B
+
+
M
r
f
d
b
+
-
e
y
human/machine system
H
u

## Slide 39
F
B
+
+
M
r
f
u
d
b
+
-
e
y
human/machine system
feedforward
feedback
McRuer, Jex IEEE Transactions on Human Factors in Electronics 1967
A Review of Quasi-Linear Pilot Models
Yu, Gillespie, Freudenberg, Cook IEEE CDC 2014
Human control strategies in pursuit tracking with a disturbance input
Yamagami, Howell, Roth, Burden IFAC CPHS 2018
Contributions of feedforward and feedback control in a manual trajectory-tracking task
H: humans use feedforward and feedback

## Slide 40
Roth, Hall, Daniel, Sponberg PNAS 2016
Integration of parallel mechanosensory and visual pathways resolved through sensory conflict
Yu, Gillespie, Freudenberg, Cook IEEE CDC 2014
Human control strategies in pursuit tracking with a disturbance input
Yamagami, Howell, Roth, Burden IFAC CPHS 2018
Contributions of feedforward and feedback control in a manual trajectory-tracking task
H: humans use feedforward and feedback
F
B
+
+
M
r
u
d
+
-
e
y
  test hypothesis:
  transcribe block diagram to algebraic equations
  solve equations for F, B
  (1.)
  (2.)

## Slide 41
experiment: manual interface
  subjects use 1-dimensional joystick device to control cursor motion to track specified reference
Roth, Howell, Beckwith, Burden SPIE 2017
Toward experimental validation of a model for human sensorimotor learning and control in teleoperation
Yamagami, Howell, Roth, Burden CPHS 2018
Contributions of feedforward and feedback control in a manual trajectory-tracking task

## Slide 42
result: humans invert first-order model
Yamagami, Howell, Roth, Burden CPHS 2018
Contributions of feedforward and feedback control in a manual trajectory-tracking task
i.e.
(first-order)
F
B
+
+
M
r
u
d
+
-
e
y

## Slide 43
Yamagami, Howell, Roth, Burden IFAC CPHS 2018
Contributions of feedforward and feedback control in a manual trajectory-tracking task
i.e.
(second-order)
result: humans invert second-order model
F
B
+
+
M
r
u
d
+
-
e
y

## Slide 44
experiment: muscle vs manual
  manual: 1-dimensional joystick
  muscle: EMG on biceps/triceps
  task: reference tracking
Yamagami, Steele, Burden CHI 2019 (submitted)
Muscle interface performance for users with and without motor impairments: decoding intent with control theory

## Slide 45
inversion error
tracking error
Yamagami, Steele, Burden CHI 2019 (submitted)
Muscle interface performance for users with and without motor impairments: decoding intent with control theory
muscle manual
muscle manual
results:

## Slide 46
nonlinear system model
  system model is simpler in (x,z) coordinates
*strict relative degree – easily satisfied for mechanical systems
  under a technical condition* we change coordinates to
  start with system model in control-affine form

## Slide 47
nonlinear inverse model
  start with simplified system model
*augment with feedback to correct for initial condition error
  to obtain inverse model, apply input ud that matches* g—th derivative of desired output yd :

## Slide 48
control with inverse models
  closed-loop dynamics have undesirable property:
  states in z are unobservable
  generally impossible to compute inverting input ud using observations of y
  by restricting system dynamics, can bypass this issue:
Robinson, Scobee, Burden, Sastry SPIE-DSS 2016
Dynamic inverse models in human-cyber-physical systems
Theorem (Robinson, Scobee, Burden, Sastry):
if system model M is infinitesimally contractive,
then feedforward input from internal model
asymptotically inverts system’s dynamics

## Slide 49
Theorem implies:
  for contractive models, trajectories x1 and x2 converge to
  feedforward input “asymptotically inverts” dynamics
inversion with contractive model M
M, M-1
input ud
output y
Robinson, Scobee, Burden, Sastry SPIE-DSS 2016
Dynamic inverse models in human-cyber-physical systems

## Slide 50
how do we enable humans to learn and control
contact-rich robot dynamics?
today’s talk:
takeaway:
humans can invert contractive dynamics
takeaway:
contractive contact-rich robot dynamics

## Slide 51
how do we enable humans to learn and control
contact-rich robot dynamics?
today’s talk:
takeaway:
contractive contact-rich robot dynamics
takeaway:
humans can invert contractive dynamics
takeaway:
humans can invert contractive dynamics
future work: experimental integration

## Slide 52
sburden@uw.edu
http://faculty.uw.edu/sburden
thank you!
ARO YIP #W911NF-16-1-0158: Predictive models for sensorimotor control of legged locomotion
NSF CPS CRII #1565529: Provably-safe interventions for human-cyber-physical systems
NSF CPS Medium #1836819:
Certifiable reinforcement learning for cyber-physical systems

## Slide 53
how do we enable humans to learn and control
contact-rich robot dynamics?
today’s talk:
contact-rich robot
terradynamics
human sensorimotor
learning and control

## Slide 54
how do we enable humans to learn and control
contact-rich robot dynamics?
today’s talk:
human sensorimotor
learning and control
contact-rich robot
terradynamics

## Slide 55
Johnson, Burden, Koditschek IJRR 2016 (arXiv:1502.01538)
A hybrid systems model for simple manipulation and self-manipulation systems
  limbs in contact with ground
  ground penetration constraints
  continuous dynamics
  impact dynamics
Muybridge 1887 (reprinted by Dover in 1957)
parsimonious models are piecewise-defined

## Slide 56
formal definitions
  limbs in contact with ground
  ground penetration constraints
  continuous dynamics
  impact dynamics
  state space is a complete Riemannian manifold with respect to the (nondegenerate) inertia tensor
  vector field is globally Lipschitz continuous:
  constraints are never tangent to one another:
  all the functions are sufficiently smooth:

## Slide 57
formal definitions
  limbs in contact with ground
  ground penetration constraints
  continuous dynamics
  impact dynamics
  constraints are orthogonal:

## Slide 58
formal definitions
  piecewise-differentiability:

## Slide 59
Ballard Archive for Rational Mechanics and Analysis 2000
The Dynamics of Discrete Mechanical Systems with Perfect Unilateral Constraints
  limbs in contact with ground
  ground penetration constraints
  continuous dynamics
  impact dynamics
Theorem (Ballard):
trajectories exist and are unique in forward time
  make the following assumptions:
  state space is a complete Riemannian manifold
  vector field is globally Lipschitz continuous
  constraints are never tangent to one another
  all the functions are sufficiently smooth

## Slide 60
Theorem (Ballard):
if limbs are compliant, final state varies continuously w.r.t. initial state
Ballard Archive for Rational Mechanics and Analysis 2000
The Dynamics of Discrete Mechanical Systems with Perfect Unilateral Constraints

## Slide 61
Burden, Revzen, Sastry IEEE TAC 2015 (arXiv:1308.4158)
Model reduction near periodic orbits of hybrid dynamical systems
Theorem (Burden, Revzen, Sastry): reduced dynamics can be smoothed
Theorem (Burden, Revzen, Sastry):
hybrid systems reduce dimension
near periodic orbits

## Slide 62
Burden, Revzen, Sastry IEEE TAC 2015 (arXiv:1308.4158)
Model reduction near periodic orbits of hybrid dynamical systems
Interpretation: ground contact performs morphological computation (reduction)

## Slide 63
Burden, Revzen, Sastry IEEE TAC 2015 (arXiv:1308.4158)
Model reduction near periodic orbits of hybrid dynamical systems
reduction
Application: n-leg polyped reduces to lateral leg-spring (LLS) after 1 stride

## Slide 64
De, Burden, Koditschek Submitted to IJRR (arXiv:1607.03795)
A hybrid dynamical extension of averaging
Theorem: effect of many steps average to a proportional controller on total energy
  height
  energy

## Slide 65
De, Burden, Koditschek Submitted to IJRR (arXiv:1607.03795)
A hybrid dynamical extension of averaging
Interpretation: viscoelastic limb performs morphological computation (averaging)
  ≈
  steps
  height

## Slide 66
Kenneally, De, Koditschek IEEE RAL 2016; http://ghostrobotics.io
generalization of averaging to multiple limbs

## Slide 67
(why) does averaging generalize?
De, Koditschek Submitted to IJRR
Vertical hopper compositions for preflexive and feedback-stabilized
quadrupedal bounding, pacing, pronking and trotting
De, Burden, Koditschek Submitted to IJRR
A hybrid dynamical extension of averaging and its
application to the analysis of legged gait stability
  bound
  trot

## Slide 68
Burden, Libby, Coogan (arXiv:1804.04122)
On contraction analysis for hybrid systems
  contractive
  expansive liftoff
  expansive impact
  contractive

## Slide 69
how do we enable humans to learn and control
contact-rich robot dynamics?
today’s talk:
human sensorimotor
learning and control
contact-rich robot
terradynamics
human sensorimotor
learning and control